## Slide 1
Development of Multi-Layer 1D divertor code and analysis of detached divertor plasmas
aSatoshi Togo, bMakoto Nakamura, cKatsuhiro Shimizu,
dTomonori Takizuka, bKazuo Hoshino, aYuichi Ogawa
aGraduate School of Frontier Science, University of Tokyo
bJapan Atomic Energy Agency, Aomori
cJapan Atomic Energy Agency, Ibaraki
dGraduate School of Engineering, Osaka University
第16回 若手科学者によるプラズマ研究会
2013/03/04-06 @Naka, JAEA

## Slide 2
Back ground
Divertor heat load
Core
Plasma
Pout
Pout ～ 90MW
(ITER)
The wetted area is a few square meters so some sort of power handling is necessary.
The divertor heat load have to be 5~6MW/m2 at most from the material point of view.
Pout ～ 500MW
(Slim-CS)
Reduction of the divertor heat load is one of the crucial issues for commercializing the fusion reactors.

## Slide 3
Divertor detachment
N. Ohno and S. Takamura, J. Plasma Fusion Res. 84, No.11, 740-749 (2008).
S. Takamura, J. Plasma Fusion Res. 72, No.9, 866-873 (1996).
Divertor detachment is thought to be a promising way.
Back ground

## Slide 4
Two-dimensional SOL-divertor code
Numerical grid for JT-60U in the SONIC simulation
The electron temperature and the parallel ion flux as a function of the mid-plane density
K. Hoshino et al., J. Plasma Fusion Res. Ser. 9, 592-597 (2010).
2D codes are used in order to estimate rigorously the performance of the divertor.
In simulating detached divertor regime, there are some quantitative disagreements with the experimental results.
Back ground

## Slide 5
Purpose of our research
Core
Plasma
Detached
Tube
Attached
Tube
X-point
Magnetic Field
0
L
x
Schematic picture of ML 1D code
The characteristics of partially detached divertor plasmas in the perpendicular direction are reproduced with only two flux tubes.
http://www.lhd.nifs.ac.jp/
We have been developing Multi-Layer (ML) 1D divertor code so as to generate an understanding of the important processes for the quantitative reproduce of (partially) detached divertor plasmas.

## Slide 6
ML 1D code
Basic equations
Mass conservation:
Momentum conservation:
Energy conservation:
Core
Plasma
Detached
Tube
Attached
Tube
X-point
Magnetic Field
0
L
x
Radial transport is included in the source terms.
Density, velocity and temperature of ion and electron are assumed to be equal, respectively.

## Slide 7
Source terms/Atomic processes
Particle source:
Momentum source:
Energy source:
ML 1D code
S. Takamura, J. Plasma Fusion Res. 72, No.9, 866-873 (1996).

## Slide 8
Boundary condition
Stagnation point (x = 0)
Divertor plate (x = L)
x=0
x=L
is the sheath heat transmission factor.
Core
Plasma
Detached
Tube
Attached
Tube
X-point
Magnetic Field
0
L
x
ML 1D code

## Slide 9
Neutral model
Particle conservation：
S. Nakazawa et al., Plasma Phys. Control. Fusion 42, 401-413 (2000).
Convection with Franck-Condon Energy
Diffusion by charge exchange reaction
Boundary condition：
Radial transport
ML 1D code
Neutralization rate

## Slide 10
Calculation condition
Simulation has been done for ASDEX-Upgrade like plasma.
A. Kallenbach et al., Nucl. Fusion 48 085008 (2008).
・Area of separatrix：40m2
・Width of the SOL：2cm
http://www.ipp.mpg.de/ippcms/eng/for/projekte/asdex/
・Minor radius a：0.6m
・Major radius R：1.7m
・Surface safety factor q：3.3
・Connection length πqR：17.6m
・Divertor leg：4.4m
・Heat flux from the core plasma：4MW
・Neutralization rate of the plate η：99%
・Impurity：Carbon, 1%, non-coronal equilibrium
ML 1D code

## Slide 11
Attached plasma solution
Diffusion by the charge exchange is assumed to be dominant.
Particle flux from the core plasma is 1.0×1021 s-1.
[/m3]
[eV]
[/m3]
X-point
Recent result

## Slide 12
ION
NEUTRAL
Core
5×1020/s
Ionization
499×1020/s
Recycled
499×1020/s
Not recycled
5×1020/s
Neutralization
504×1020/s
At such temperature, volume recombination can’t dominate ionization so that detachment doesn’t occur.
Heat loss is too small to dissipate all of the heat flux from the core so that the temperature near the plate is relatively high.
[W]
Heat flux
Core
Imp.
CX
Ioniz.
Recomb.
[/s]
Particle flux
Ioniz.
Core
Recomb.
Recent result
Attached plasma solution

## Slide 13
The gradient of the neutral density profile near the plate is negative implying neutral flows toward the plate there.
[/m3]
[eV]
[/m3]
X-point
Recent result
Detached plasma solution
If radial neutral loss is large enough, τn~10-4 s, particle balance is accomplished and steady state solutions appear.

## Slide 14
[W]
Heat flux
Core
Imp.
CX
Ioniz.
Recomb.
Recomb.
Particle flux
Ioniz.
Core
[/s]
Recent result
Heat loss is large enough to dissipate all of the heat flux from the core so that the temperature near the plate is relatively low.
The temperature is low enough for volume recombination to dominate ionization so that detachment occurs.
ION
NEUTRAL
Core
2.5×1022/s
Ionization
6.2×1022/s
Radial loss
2.5×1022/s
Recombination
8.7×1022/s
Detached plasma solution

## Slide 15
Conclusion
・ML 1D divertor code has been developed. During the last year, numerical neutral model was introduced and numerical scheme was improved. The detached regime has been successfully reproduced.
・Heat and particle balance in both attached and detached regime have been investigated indicating that the difference in the particle balance between attached and detached regime might be related to the formation of partially detached divertor plasma.
・To distinguish the mechanism of neutral transport by means of their generation is our future work.