## Slide 1
LHDにおけるIRVBを用いた
プラズマ輻射計測の現状
(3次元輻射計測の開発)
Ryuichi Sano1, Byron J. Peterson2, Masaru Teranishi3, Naofumi Iwama2, Masahiro Kobayashi2, Kiyofumi Mukai2, Shwetang N. Pandya1
1Graduate University for Advanced Studies, 2NIFS and 3Hiroshima Institute of Technology
若手科学者によるプラズマ研究会 2014.03.05-07

## Slide 2
Motivation
Radiation mainly occurs outside of the LCFS.
→1 dimensional assumption can not be applied.
→3D or 2D measurement is required.
IRVBs(IR imaging Video Bolometer) have many channels (500-1000ch/IRVB).
-This advantage will be effective for tomography
-In LHD and KSTAR etc.
DEMO or ITER →reduction of the heat flux to the divertor is important.
Plasma detachment is planned with enhanced radiation for the reduction of heat flux.
3D radiation measurement using with tomography is planned in LHD

## Slide 3
Plasma radiation
(Far IR～soft Xray)
Heat radiation
(IR)
Metal foil
Plasma
Aperture
IR window
IR camera
Vacuum
vessel wall
IR imaging video bolometer (IRVB)
Temperature
Radiation Image
Solve heat
diffusion
equation
Pt, blackened

## Slide 4
6.5-L (30x22 ch)
(100 fps)
6-T(36x28 ch)
(100 fps)
10-O(36x28 ch)
(100 fps)
6.5-U(26x20 ch)
(50 fps)
10-O
6-T
6.5-U
6.5-L
4 IRVBs are installed in LHD

## Slide 5
IRVBs can measure spatial and temporal radiation changes
Poloidal
Toroidal
Toroidal
Poloidal
Poloidal
Toroidal

## Slide 6: Tomography (Inverse calculation)
Prad,j :Absorbed power on each detector
hj,k :The geometry matrix as a projection matrix
Sk :The radiation intensity from the plasma-voxel
j :Index of detector channel
k :Index of plasma-voxel
3D profile
Geometry matrix
Measured (IRVB)
Measurement
Tomography

## Slide 7
LHD plasma
Mean minor radius: 0.6m
Major radius: 3.9m
Plasma voxels:
Horizontal: 5 cm
50 divisions (2.5 m < R < 5.0 m)
Vertical : 5cm
52 divisions (-1.3 m < Z < 1.3 m)
Toroidal: 1 degree
360 divisions
Total number of plasma voxels
:50x52x360=936,000
Total number of IRVB channels
:3,196ch
LHD plasma divided into voxels for 3D tomography
IRVB channels << Plasma voxels

## Slide 8
Non plasma voxels eliminated using EMC3-EIRENE prediction of radiating volume
936,000 → 263,220
Total number of plasma voxel is reduced by mask
radiation region
Non-radiation region

## Slide 9
Helical periodicity
・The plasma repeats itself
every 18 degree toroidally.
S(R, φ , Z) = S(R, π/5- φ,-Z)
Total number of plasma voxels reduced
:263,220/20 = 13,161
Assumption of Helical periodicity reduces number of plasma voxels
Each plasma voxel should be seen by at least one IRVB channel
Number of IRVBs is just 4
→Fields of view of IRVBs can not cover entire torus
→ Assumption of helical periodicity is employed.
Total number of IRVB channels
:3,196 ch

## Slide 10
Reconstruction by ART (Algebraic Reconstruction Techniques)
ART: Iterative method with feedback for every sight line.
P : IRVB signal
H : Projection matrix
S : Plasma radiation at voxel
H
P
H
P
P
HT
S2
S1
S
S2
H
P
P
S3
Iteration
S1
HT
S2
Calculation time=(2 hours/ frame)

## Slide 11
Test image reconstructed by ART (from simulated profile)
Test radiation profile, S
(calculated by EMC3-EIRENE)
Reconstructed profile, S’
Incident radiation at 6.5-L, P
(from EMC3-EIRENE)
ART
Test hollow profiles is reproduced through reconstruction

## Slide 12
Reconstruction by SVD (Singular Value Decomposition)
SVD
U : Left singular vector of H
V: Right singular vector of H
W: Diagonal matrix of singular value
H (13161 x 3196) was successfully decomposed
H+: Pseudo-inverse matrix of H
(4 minutes / frame)
P
=
H
S
P
=
H-1
S
IRVBs signal (3196)
Plasma radiation (13,161)
P : IRVB signal
H : Projection matrix
S : Plasma radiation at voxel

## Slide 13
Test image reconstructed by SVD (from simulated profile)
Test radiation profile, S
(calculated by EMC3-EIRENE)
Reconstructed profile, S’
Incident radiation at 6.5-L, P
(from EMC3-EIRENE)
SVD
Like ART profiles, but negative values are produced.

## Slide 14
#120930
Reconstructed 3D profile from experiment (SVD method)
Reconstructed 3D profile from experiment (ART method)
Reconstructed 3D profile from experiment (ART method)
ART results has localized radiation at the edge plasma
#120930
・Radiation is localized in the edge region.
・Calculation takes 2 hours.
・There are no negative values.
・Radiation from core region may be ghosts.

## Slide 15
SVD results has strong radiation in core.
・Radiation is not localized in a certain region.
・Calculation takes 4 minutes.
・Large negative values are produced.
Reconstructed 3D profile from experiment (SVD method)
#120930

## Slide 16
Summary
3D tomography techniques for radiation measurement using 4 IRVBs with ART and SVD are developed in LHD
・ART method
Features of test profile reproduced through reconstruction.
But minor ghosts remain in core.
ART takes 30 times more calculation time than SVD.
・SVD method
Features of test profile reproduced through reconstruction.
But strong ghosts remain in core.
Both methods need more improvement
Measurement of enhanced radiation for detachment or starting phase of radiation collapse.

## Slide 19
Reconstructed (GCV is considered)
(A)
(C)
(B)
Chart: g
4e-16
1.9e-13
2.7e-9
1.91e-13
e**2

## Slide 20
Reconstruction by ART (Algebraic Reconstruction Techniques)
H: Projection matrix
a: Weight parameter for feedback
k: Counts of iterations
f: 3D radiation profiles
g: IRVB data
M: total number of IRVB channels
M (3,196) times
ART: Iterative method with feedback for every sight line.
(N)th IRVB channel
Current 3D radiation profile
Original
(N)th IRVB channel
H
P : IRVB signal
H : Projection matrix
S : Plasma radiation at voxel
HT
N=1～M

## Slide 21
Characterization of foil thermal properties needed for calibration
Conventional method gives only tf
  Developed method gives tf and ε by iterative convergence
Ryuichi SANO et al., Plasma and Fusion Res. 7 2405039 (2012)
Radiation power
Foil temperature
Solve Heat
diffusion equation
IRVB measurement
Heat diffusion equation
Foil parameters (not uniform)
Foil thickness : tf
Emissivity : ε
Thermal diffusivity: κ

## Slide 22
Reconstructed by SVD
(Collapse like)
Radiation profile on poloidal cross section
(Collapse like)
・Reconstructed radiation profile has tendency of original profile.
・More constraints or filter is required.
Reconstructed image by SVD (from special profile)
Reconstructed by SVD
(uniform)
Radiation profile on poloidal cross section
(uniform)
Incident radiation
(from EMC-3)
Incident radiation
(from reconstructed)
Incident radiation
(from EMC-3)
Incident radiation
(from reconstructed)

## Slide 23: IRVB signal and geometry matrix calculation
Absorbed power at each detector channel
Prad,j :Absorbed power on each detector
hj,k :The geometry matrix as a projection matrix
Sk :The radiation intensity from the plasma-voxel
j :Index of detector channel
K :index of plasma-voxel
Geometry matrix (projection matrix)
hj,k : The geometry matrix as a projection matrix
Vi,j,k : Volume of FOV(field of view) sub-voxel
Ωi,j,k : solid angle of the detector with respect to the sub
FOV sub-volume
k : Index of plasma-voxel
i : Index of FOV sub-volume
j : Index of detector channel

## Slide 24
IRVBs can take spatial and temporal radiation changes