## Slide 1
SOL-Divertor Plasma Simulations by Introducing Anisotropic Ion Temperatures and Virtual Divertor Model
非等方イオン温度と仮想ダイバータモデルを導入したSOL-ダイバータプラズマシミュレーション
Satoshi Togo, Tomonori Takizukaa, Makoto Nakamurab,
Kazuo Hoshinob, Kenzo Ibanoa, Tee Long Lang, Yuichi Ogawa
Graduate School of Frontier Sciences, University of Tokyo, 5-1-5 Kashiwanoha, Kashiwa 277-8568, Japan
aGraduate school of Engineering, Osaka University, 2-1 Yamadaoka, Suita 565-0871, Japan
bJapan Atomic Energy Agency, 2-166 Omotedate, Obuchi-aza, O-aza, Rokkasho 039-3212, Japan
第18回若手科学者によるプラズマ研究会
2015/03/04-06

## Slide 2
Motivation
The parallel ion viscous flux -ηi,//(∂V/∂s)
・the approximated form of the stress tensor p
(π = 2n(Ti,// - Ti,⊥)/3)
・derived under the assumption that π << nTi.
A. Froese et al., Plasma Fusion Res. 5 (2010) 026.
The kinetic simulations showed a remarkable anisotropy in the ion temperature even for the medium collisionality.
The SOL-divertor plasma code packages (SOLPS, SONIC, etc.)
・used to estimate the performance of the divertors of future devices
・some physics models are used in the plasma fluid model (e. g. viscosity)
・physics models are valid in the collisional regime
parallel momentum transport equation (1D)
The boundary condition Mt = 1 has been used in the conventional codes.
However, the Bohm condition only imposes the lower limit as Mt ≥ 1.
collisional
collisionless
Result from PARASOL code

## Slide 3
Momentum Eq. & Virtual Divertor Model
Introduction of the anisotropic ion temperatures, Ti,// and Ti,⊥, to the fluid model
・changes the momentum transport equation into the first-order
・makes the explicit boundary condition at the divertor plate unnecessary
conventional codes (effective isotropic Ti)
Parallel-to-B component of the Boltzmann equation
Instead of the boundary condition Mt = 1, we modeled the effects of the divertor plate and the accompanying sheath by using a virtual divertor (VD) model.
P. C. Stangeby, The Plasma Boundary of Magnetic Fusion Devices.
Flow velocity is not determined by downstream ‘waterfall’ but by upstream condition.
(isotropic Te is assumed)

## Slide 4
Plasma Fluid Eqs. & Artificial Sinks in VD
Eq. of continuity
Eq. of momentum transport
Eq. of parallel (//) ion energy transport
Eq. of perpendicular (⊥) ion energy transport
Eq. of electron energy transport
Artificial sinks in the virtual divertor (VD) region
S. Togo et al., J. Nucl. Mater. (2015) in Press.
Periodic boundary condition
※according to the image of a waterfall

## Slide 5
Plasma Fluid Eqs. & Artificial Sinks in VD
Eq. of continuity
Eq. of momentum transport
Eq. of parallel (//) ion energy transport
Eq. of perpendicular (⊥) ion energy transport
Eq. of electron energy transport
Ion pressure relaxation time trlx = 2.5ti.
(E. Zawaideh et al., Phys. Fluids 29 (1986) 463.)
Because the parallel internal energy convection is 3 times as large as the parallel internal energy, Ti,// becomes lower than Ti,⊥.
c = 0.5 is used.
Heat flux limiting factors;
ai,// = ai,⊥ = 0.5, ae = 0.2
are used.
qseff = (1/qsSH + 1/asqsFS)-1
Neutral is not considered at first.

## Slide 6
Results (Anisotropy of Ti and the Profiles)
n (1019 /m3)
M
Ti,// (eV)
Ti,⊥ (eV)
Te (eV)
weakly collisional case
collisional case
VD
Anisotropy of Ti vs normalized MFP of i-i collision
Gsep and Psep are changed.

## Slide 7
Results (Bohm condition M* = 1)
Time evolutions of M* for various tVD
M* saturates at ~ 1 independently of the value of tVD.
Characteristic time tBohm depends on tVD and 2 orders shorter than the quasi-stationary time ~ 10-3 s.
For the simulations of transient phenomena, such as ELMs, tBohm has to be smaller than their characteristic times.
T. Takizuka and M. Hosokawa, Contrib. Plasma Phys. 40 (2000) 3-4, 471.
ga = 3 for adiabatic, collisionless sound speed
PARASOL

## Slide 8
Results (Sheath heat transmission factors)
From the sheath theory,
For Ti = Te,
ge ≈ 5 for H+ plasma
ge ≈ 5.3 for D+ plasma
Relation between sheath heat transmission factors and gs
gi scarcely depends on gs because convective heat flux dominates conductive one.
ge can be adjusted to the values based on the sheath theory by VD model.
Boundary conditions for the heat flux at the divertor plate in the conventional codes;

## Slide 9
Results (Dependence of the profiles on tVD)
Decay length in VD region: Ld ~ VttVD.
As long as Ds < Ld < LVD, the profiles in the plasma region do not change.
If Ld > LVD (when tVD = 5×10-5 s in figure), the profiles become invalid.
If Ld < Ds, numerical calculation diverges.
The profiles just in front of the divertor plates are affected by the artificial sinks in VD region due to numerical viscosity.
This problem will be solved by introducing a high-accuracy difference scheme and an inhomogeneous grid.

## Slide 10
Results (Supersonic flow due to cooling)
C = (RG/Rp)(Tt/TX)1/2, T = Ti,// + Te(,//)
M = V/cs
T. Takizuka et al., J. Nucl. Mater. 290-293 (2001) 753.
(at the plate)
(at the X-point)
Isothermal sound speed
Cooling term Qe = -nTe/trad is set in the divertor region.
RG = Rp = 1
Mt well agrees with the theory.
The reason for MX > 1 is under investigation.
PARASOL

## Slide 11
Results (Ion Viscous Flux vs Stress Tensor)
Two kinds of ion viscous flux,
are compared to the stress tensor,
pdef = 2n(Ti,//-Ti,⊥)/3, in the particle-source-less-region (s = 20.005 m) and particle-source-region (s = 17.005 m).
pBR becomes 2~3 orders larger than pdef as lmfp/L becomes large.
b = 0.7 :viscosity limiting factor
In the particle-source-region, the correlation between plim and pdef becomes worse especially in the collisional region.
In the particle-source-less region, plim with b = 0.7 comparably agrees with pdef. However, b depends on the anisotropy of ion pressure which might change with the neutral effects.
Therefore, it is necessary to distinguish between Ti,// and Ti,⊥.

## Slide 12
Self-Consistent Neutral Model (in VD)
Diffusion neutral
Recycling neutral (inner plate)
Recycling neutral (outer plate)
periodic boundary condition
conventional
present
boundary condition
(Eq. of continuity for plasma)
tn,diffVD : input
The coordinate x
: poloidal direction x = (Bp/B)s.
Recycling neutral
Diffusion neutral

## Slide 13
Self-Consistent Neutral Model (in Plasma)
Diffusion neutral
Recycling neutral (inner plate)
The coordinate x: poloidal direction x = (Bp/B)s.
Recycling neutral (outer plate)
where VFC = (2εFC/mi)1/2 with Franck-Condon energy εFC = 3.5 eV.
T. Takizuka et al., 12th BPSI Meeting, Kasuga, Fukuoka 2014 (2015).
aL : input

## Slide 14
Atomic Processes
Diffusion neutral
Recycling neutral (inner plate)
Recycling neutral (outer plate)
(εiz = 30 eV)
Source terms for plasma:
(θ = Bp/B)
(Ti = (Ti,// + 2Ti,⊥)/3)

## Slide 15
Result (Low recycling condition)
Ti,//
Te
Ti,⊥
nn,recy
nn,diff
aL = 1
Recycling rate ~ 0.17
Ti,///Ti,⊥ ~ 0.6
Recycling neutral dominant
X-point
Near the plate

## Slide 16
Result (High recycling condition)
X-point
Ti,⊥
Te
Ti,//
nn,recy
nn,diff
Near the plate
aL = 0.1
Recycling rate ~ 0.92
Ti,///Ti,⊥ ~ 1
Diffusion neutral dominant

## Slide 17
Conclusions
1D SOL-divertor plasma model with anisotropic ion temperatures has been developed. In order to express the effects of the divertor plate and the accompanying sheath, we use a virtual divertor (VD) model which sets artificial sinks for particle, momentum and energy in the additional region beyond the divertor plate. In addition, VD makes the periodic boundary condition available and reduces the numerical difficulty.
For simplicity, the symmetric inner/outer SOL-divertor plasmas with the homogeneous magnetic fields are assumed. In order to simulate more general asymmetric plasmas with the inhomogeneous magnetic fields, the effects of the plasma current and the mirror force have to be considered. In addition, it is necessary to introduce a high-accuracy difference scheme and an inhomogeneous grid in order to avoid the numerical errors at the divertor plate. These are our future works.

## Slide 18
DmVD & gi,// in VD region
DmVD and gi,// in VD region have Gaussian shapes.
The length of V-connection-region L0 = 1.6 m.

## Slide 19
Results (Bohm condition)
T. Takizuka and M. Hosokawa, Contrib. Plasma Phys. 40 (2000) 3-4, 471.
Mach profiles for various Ds
ga = 3 for adiabatic, collisionless sound speed
M* ≈ 1 with no cooling effects.
VD
Plasma
The effect of artificial sinks in VD region numerically diffuses in the plasma region.

## Slide 20
Appendix ~ Collisionless Adiabatic Flow ~
1D equations in the collisionless limit;
Refer to Sec 10.8 of Stangeby’s text

## Slide 21
The effect of gs on gt (heat transmission factor)
The boundary condition for the heat flux at the divertor plate in the usual codes;
The heat transmission factors, gi and ge, are input parameters.
The VD model, however, does not use this boundary condition but the periodic boundary condition with the cooling index gs (s ∈ i//, i⊥, e). Therefore gi and ge are back calculated using these relations.
The conduction heat fluxes are limited by the free-streaming heat fluxes with limiting coefficients as as qseff = (1/qsSH + 1/asqsFS)-1.
Thus the effective conduction heat fluxes are smaller than the free-streaming heat fluxes times limiting coefficients asqsFS so that gt has the maximum.

## Slide 22
Calculation condition
Calculation condition | 
H plasma and ni = ne = n | 
Symmetric inner/outer SOL | 
Length of the plasma L | 44 m
SOL width d | 2 cm
Separatrix area | 40 m2
Particle flux from core Γsep | 1~5×1022 /s
Heat flux from the core Psep | 1~4 MW
Cooling index for i,// | 1
Cooling index for i,⊥ | 1.2
Cooling index for e | 2.5
tVD | 5×10-6 s
Heat flux limiter for ion | 0.5
Heat flux limiter for electron | 0.2

## Slide 23
M. Wischmeier et al., J. Nucl. Mater. 390-391, 250 (2009).
Comparison of results (EXP vs SIM)
Edge transport code packages, such as SOLPS and SONIC, are widely used to predict performance of the scrape-off layer (SOL) and divertor of ITER and DEMO. Simulation results, however, have not satisfactorily agreed with experimental ones.
Discrepancy

## Slide 24
Why does Ti,// become lower than Ti,⊥?
Reduced eq. of parallel (//) ion energy transport
Reduced eq. of perpendicular (⊥) ion energy transport
Integration over x from the stagnation to x yields,
By considering the kinetic energy term and force term, Ti,///Ti.⊥ ~ 0.2.
Eq. of parallel (//) ion energy transport

## Slide 25
Qualitative derivation of the viscous flux
Simplified system equations
(A)
(B)
(C)
(E)
From (C) – (D)
(D)
(E)’
Assumption of p << nTi
(B)’
By (A) and (B)’, LHS of (E)’ becomes
Then

## Slide 26
Necessity of artificial viscosity term
conservation of ion particles
conservation of parallel plasma momentum
When V is positive, RHS becomes positive. If V becomes supersonic, dV/dx becomes positive and V cannot connects.
artificial viscosity term

## Slide 27
Discretization
general conservation equation
full implicit
upwind
central
discretization scheme
staggered mesh (uniform dx)

## Slide 28
Calculation method
matrix equation
(ex. N = 5)
Matrix G becomes cyclic tridiagonal due to the periodic boundary condition. This matrix can be decomposed by defining two vectors u and v so that
where A is tridiagonal.

## Slide 29
Calculation method
Sherman-Morrison formula
where and .
y and z can be solved by using tridiagonal matrix algorithm (TDMA).
calculation flow
Ion // energy
Elec. energy
Momentum
Particle
No
Yes
The number of equations can be changed easily.
Ion ⊥ energy

## Slide 30
Continuity of Mach number
conservation of ion particles
conservation of parallel plasma momentum
Due to the continuity of Mach number, RHS has to be zero at the sonic transition point (M = 1).
RHS > 0
RHS ≦ 0
Sonic transition has to occur at the X-point when T = const.
O. Marchuk and M. Z. Tokar, J. Comput. Phys. 227, 1597 (2007).

## Slide 31
Result (particle flux & Mach vs nsep)
Γt ∝ nsep
→ accords with conventional simulations
Supersonic flow (Mt > 1)
→ observed when nsep is low
Subsonic flow (Mt < 1)
→ observed when nsep is high
→ numerical problem?
Larger nsep (like detached plasmas) is future work.

## Slide 32
Result (Mach number near the plate)
Plasma
VD
M > 1 is satisfied in the near-plate VD region.
Smaller Δs results in a better result. → Numerical problem?
Δs = 2cm
Δs = 5cm
Near the plate

## Slide 33
Result (Mt vs nsep)
The recycling neutrals are not ionized or do not experience the charge exchange near the plate (red line).